Autumn Sound Specs:

Autumn will bring their own FOH engineer

The venue has to supply an experienced system engineer.

P.A.

- A class A - P.A. that can produce 110dba (slow) undistorted from 20hz to 20khz at the FOH mix position and spread equally throughout the hall (If necessary use delay and/or infill speakers).

FOH.

- a minimum of 32 channels (xl series, H2000)

- 10 VCA groups

- 8 Sub groups

- 8 Aux sends

- 2 x 31-bands EQ (Klark/XTA)

- 6 x Gate (Drawmer/BSS), 8 x Compressor (DBX/BSS).

- 1 x Vocal Reverb, 1 x Multi FX, Delay (Lexicon PCM70/90/300/480, TC

Electronic M2000/M3000/M5000/Reverb4000/2290/D2, Yamaha

SPX900/990/2000).

MON.

- Autumn will bring its own monitor mixing system.

- This monitor system can be routed from the stagebox (split). Autumn can supply a splitter (XLR multicable (~4mtrs).

- Alternatively, the split can be made in the monitor system itself. In that case the channels that need splitting should be connected to the monitor system first.

- See channel list on page 3 for details.

- The monitor system should be placed in a spot that is accessible to all band members during the show.

- In case of inability to use the mobile monitor system, the in-house monitor system should contain a minimum of 24 channels

- a minimum of 6 sends with 31-bands EQ (Klark/XTA)

- 4 groups of two identical bi-amped wedges (Synco/LAcoustics/D&B)

- 2 xlr lines for (wired) in-ear systems (at Drum and Key position)

For any questions regarding the sound for Autumn:

Mats van der valk

matsvdvalk@gmail.com

+31630387970

Autumn stageplot

=  220v power outlet

Voc J, inpt 17    Voc Marjan, inpt 19  Voc R, inpt 18  Voc M, inpt 16

| Chanel | Instrument | mic/Di | Split to inEar rack | Comment |
| --- | --- | --- | --- | --- |
| 1 | Kick In | 91Beta |  |  |
| 2 | Kick Out | D6 | ✔️ |  |
| 3 | Sn Top | Beyer 201/ sm57 | ✔️ |  |
| 4 | Sn Bot | sm57 |  |  |
| 5 | HH | Condenser | ✔️ |  |
| 6 | T | 904 | ✔️ |  |
| 7 | FL1 | 904 | ✔️ |  |
| 8 | FL2 | 904 | ✔️ |  |
| 9 | - |  |  |  |
| 10 | Ride | Condenser | ✔️ |  |
| 11 | OH L | Condenser | ✔️ |  |
| 12 | OH R | Condenser | ✔️ |  |
| 13 | Bass Di | XLR | ✔️ |  |
| 14 | Bass Mic | M88/ 421 |  | Only at headliner shows |
| 15 | Gtr 1 Dir | XLR | ✔️ |  |
| 16 | Gtr 1 Mic | Heil PR30/ sm57 |  | Only at headliner shows |
| 17 | Gtr 2 Dir | XLR | ✔️ |  |
| 18 | Gtr 2 Mic | Heil PR30/ sm57 |  | Only at headliner shows |
| 19 | Gtr 3 Dir | XLR | ✔️ |  |
| 20 | Gtr3 Mic | Heil PR30/ sm57 |  | Only at headliner shows |
| 21 | Key L | XLR from rack |  |  |
| 22 | Key R | XLR from rack |  |  |
| 23 | - |  |  |  |
| 24 | - |  |  |  |
| 25 | Voc SR (Jens) | sm58 | ✔️ |  |
| 26 | Voc CL (Ronald) | sm58 | ✔️ |  |
| 27 | Voc SL (Mats) | sm58 | ✔️ |  |
| 28 | LEAD voc (Marjan) | OWN Wireless Sm58 | ✔️ |  |

# Text boxes

Keyboard riser

Input: 14-15

Drum riser

Input: 1-9 + 21 / 22

Monitor mixer

Autumn

Mon 2

Mon 1

Bass, Inpt

13 & 20

Gtr amp

Inpt 10

Gtr amp 1 / 2

Inpt: 11-12

Mon 5

Mon 3

Mon 4